## Slide 1: PyLoader Tutorial
How to use Python to write tests for and interface with freeLoader machines
Updated 8/12/14
Written by Anthony McNicoll (am859@cornell.edu)

## Slide 2: freeLoader Background
Applies + measures compressive and tensile loads
Motor is Dynamixel MX-64, communicates over serial
Load cell + interface from Loadstar, also over serial
Highly configurable

## Slide 3: Python Background
Legible, easy to learn, well-documented, open source
Python 2.xx simply installs using one .exe file
Edit with text editor, run by double-click or command
Object oriented:
  Files may contain scripts that just run
  Files may also define functions
  Files may also define classes:
    Classes represent objects
    They have attributes (values of interest)
    They have methods (functions operating on that class)
Functions and classes can be imported into other files
Careful: Code blocks are defined using tabs, not braces

## Slide 4: What It Looks Like
Block comments with “””, single line with #
Definitions, ifs, loops defined with colon and indented (4 spaces) code
Only data types of interest are string, int (round numbers) and float (decimal numbers)
Variables are declared implicitly, like MATLAB

## Slide 5: Code Structure Overview

## Slide 6: Using the Freeloader Class
Use import statement:
Create a Freeloader object and connect:
Use any of the methods defined for a Freeloader:
from freeloader import Freeloader, FreeloaderError
machine = Freeloader() # machine could be any name
machine.autoconnect() # will find motor, cell for you
machine.start_motor(30, down = True) # Go down at 30 mm/min
machine.stop_motor() # Stop the motor
machine.get_raw_encoder() # Get pos. as 0-4096
machine.get_linear_position() # Get pos. as mm
machine.reset_linear_position() # Set pos. as mm to 0
machine.read_raw_cell() # Get string from load cell
machine.read_cell() # Get load as float
machine.disconnect() # Close serial ports

## Slide 7: Writing a Test using BasicTest, Part I
Things to understand:
  A BasicTest is a class containing useful methods, like collect_until(), that make test writing easy
  To take advantage of these, you must write a new class which inherits from a BasicTest.
  From there, you must override (re-define) whatever you need for your test. At minimum, the run_test() routine must be defined.
Start by copying source code from the closest existing test
  As of this writing, a tension test is available
Give your new class an appropriate name:
class NewCompTest(BasicTest): # Compression test

## Slide 8: Writing a Test using BasicTest, Part II
If collecting more than load and position, you will need to override (re-define) the default collect_data method. For instance, imagine reading an analog pressure sensor:
To access the test’s Freeloader, use self.fl
You can use any Python code you want here. For example, you can connect to an Arduino and collect data from it as well.

## Slide 9: Writing a Test using BasicTest, Part III
Define the run_test() routine. First, define columns and initialize the data set:
If needed, collect data from user:
Define test procedure using commands on next slide.
Call self.fl.disconnect() to safely stop things.
Build a header string if needed (see tensiontest.py)
Call self.write_file(header) to write data to a file.
self.set_columns([‘time’,’position’,’load’,’pressure’])
self.initialize_data()
max_dist = float(raw_input(“Move no further than: “))

## Slide 10: BasicTest Method Quick Reference
point = self.collect_data() # get a fresh data point
lload = self.get_last_value(‘load’) # Get last value of ?
fpres = self.get_first_value(‘pressure’) # Get first value of ?
lpoint = self.get_last_point() # Get last point as list
fpoint = self.get_first_point() # Get first point as list
all_load = self.get_all_values(‘load’) # Get list of recorded ?
self.data # 2D list of all data
self.Initialize_data() # Call at test start
self.run_test() # Never call
self.collect_until(‘distance’,’lessthan’,20) # Collect until condition
self.collect_for(2.3) # Collect for time
self.wait_until(‘load’,’greaterthan’,25) # Wait until condition
self.wait_for(5) # Wait for time
self.collect_until_keyboard() # Collect until key press
self.wait_for_keyboard() # Wait for keyboard
self.write_file(“Time,Position,Load,Pressure”) # Write data file
Look at the HTML pages in the Documentation folder for complete descriptions of every method and available arguments.

## Slide 11: Quickstart Python Tips
Python 3 is “newer” but not as well supported as Python 2.XX, so stick with that. I used Python 2.7. Download and install that, as well as pySerial, which are both exe’s.
You can just use Sublime Text to edit code if you have it, or Notepad++. Python programs can run by simply double-clicking the source file.
Google something like “Notepad++ Python Tabs Spaces” and make sure your editor uses spaces for tabs
For debugging, it’s useful to open a command prompt, cd to the directory your code is in, and run a command like “python basictest.py”. If there is a syntax error or exception, it will stay on the screen so you can investigate it. In Sublime, you can also hit Ctrl+B.